Making an Enlargement

- Select the most successful image from your contact sheet, and remove the negative from your plastic negative protector sheet. Do not cut your negative!!!

- Place the negative in the negative carrier emulsion side down (dull side facing down)

- Turn on enlarger on focus mode and place your easel underneath the light using the correct size easel.

- Raise and lower the enlarger using the knobs on the back shaft of the enlarger until your picture fills up the easel space. The light should overlap all the edges of the frame.

- Make sure your aperture is open all the way with the most light showing, this would be the largest opening but the smallest number. Focus the image using the knob closest to you on the enlarger. (sometimes it is easier to move the easel away from the image and use the white board to focus.)

- Close APERTURE, SEE WALL FOR CORRECT STOP

- Place the easel back where it belongs and turn off the enlarger. Make sure the image extends to the edges of the easel!!!!!! Turn enlarger off!

- Switch the timer from focus mode to time mode. Set timer for 18 seconds (more time for larger paper)

- If you are using 5x7 paper use an entire sheet cut the paper in half lenthwise, if you are using 8x10 cut your paper into strips and place either one strip or your paper under in the easel. ( I like to cut a couple pages up at once so I have them for later)

- Hold a piece of cardboard over the image, only exposing about a 1 ½ inch for 3 seconds, move the cardboard over 1 ½ inch wait 3 seconds, move again, do this until you have moved it five times letting each strip have 3 seconds each.

- Process the print in the chemicals, developer, stop, rinse, fix 1min, rinse.

- Take the image out into the light and see which exposure time looks the best, then put it back in the fixer.

- Go back into the darkroom, set your timer for the time you figured out.

- Put a full piece of paper in your easel. Write the F-stop and the Aperture on the back.

- Expose it

- Develop it!

Cutting Negatives

1. Find a clean area to work

2. Lay out your roll of negatives

3. Look at your negatives for images that look bad, those are the ones you want on the ends if at all possible, because before you get the hang of it, you will probably get fingerprints on these negatives.

4. You are cutting your negatives in strips of five, because this is what fits in your negative holder.

| Like this! |  |  |  |  |
| --- | --- | --- | --- | --- |

5. If you end up with 6 negatives left…what should you do????

Cut them 3 and 3 You never want to end up with only one or two negatives, this makes them very difficult to handle and it is very likely that they will get ruined.

Once your negatives are cut you carefully put them in your negative holder and then store the negative holder in a ziplock bag.